## Slide 1
Neighbourhood-aware misbehaviour detection for V2X
Final results on 14 attack types, extended to 18 with Sybil
Evaluated on the VeReMi Extension benchmark (simulated traffic, Zenodo 20090854)
Notes: Final update. All numbers are on a simulated benchmark, not real-world traffic. Paper: paper/main.pdf (IEEE conference, 6 pages, 18 references).

## Slide 2
The idea: judge a sender by its neighbours
Problem
Vehicles broadcast position, speed and heading. A misbehaving vehicle sends false data (wrong position, speed, a fake stop) that can mislead the cars around it.
Our approach
A small transformer looks at each sender over time and at the other senders nearby (neighbour attention), so it can spot a sender whose claims do not fit its surroundings.
Notes: Per-sender view vs neighbourhood-aware view; neighbour attention is the part we test with an ablation.

## Slide 3
What was built
1
Data
VeReMi Extension: 14 of 19 attack types for the main results; extended to 18 of 19 with the four Sybil attacks (RandomSpeedOffset archive excluded as mislabeled)
2
Splits
Train 109,823 / validation 29,547 / test 68,971 windows; 2 seeds
3
Final model (v2)
Transformer, 144k parameters, temporal + neighbour attention; 9 claim values + 10 plausibility checks per message
4
Checks and training
Kinematics, road map learned from honest traffic, nearest other claim, self-repeat, copied trail; training adds injected lies (offset, fake stop); receiver-side memory

## Slide 4
Results on the test set (14 attacks)
Model | Labels | Precision | Recall | F1 | Accuracy
Speed-check rule | vehicle / message | - | - | 78.9 / 80.0 | -
First model (no checks) | vehicle | 98.4 | 91.6 | 94.9 | 96.9
v2 | vehicle | 98.65 | 95.41 | 97.01 | 98.14
v2 + memory | vehicle | - | 96.09 | 97.12 | 98.20
v2 | message | 98.65 | 97.12 | 97.88 | 98.69
v2 + memory | message | 98.16 | 97.78 | 97.97 | 98.74
False-positive rate: v2 0.60% (first model 0.7%)
Message labels count an attacker only in windows where it sent a falsified message (dataset ground truth). Vehicle labels count every window of an attacker vehicle, including its honest-looking ones, so recall is lower.
All values in %. Mean of 2 seeds. '-' = not reported for that row.
Notes: Both label schemes are shown on purpose; message labels match how the dataset marks lies, vehicle labels are the stricter view.

## Slide 5
What neighbour attention adds
Small but real
+0.3 F1 points (95% CI about [0.2, 0.4]). Significant on 8-10 of the 14 attacks.
Fewer false alarms
False-positive rate drops from 0.90% to 0.60% with neighbour attention.
Fails with attacker majority
When attackers are most of a sender's neighbours the gain shrinks and turns negative (-0.004 within-attack). First model: +0.071 down to -0.023.
Notes: Be upfront: neighbour attention is a modest gain, and it depends on honest neighbours being the majority.

## Slide 6
How fast attackers are flagged (v2)
0.9 s
mean time to first alarm
0 s
median time to first alarm
96%
of attacker-receiver pairs flagged
Most attackers are caught in the first window they appear in; a few take longer and pull the mean up.
Notes: Latency counts from the first window that contains the attacker, per receiver.

## Slide 7
Stress test: colluding attackers
Consistent lie (colluders) | First model | v2
50 m position offset | <= 0.04 | 0.83-0.86
Fake stop | <= 0.04 | about 0.70
Spoofed convoy (never seen in training) | <= 0.04 | 0.87-0.90
Offset along the road (map-aware) | <= 0.04 | 0.23-0.25
Convoy on own road (map-aware) | <= 0.04 | 0.36-0.48
Colluder recall at a matched 1% false-positive rate. Coordinated convoys also raised the first model's honest false-positive rate from 0.9% to 3.0%.
Lies that stay on the road map are still hard: they need an independent signal (signal strength, sensors, roadside units).
Notes: Injected collusion on top of VeReMi; the dataset itself has no colluding attackers.

## Slide 8
Against the reference paper
Chart: 
| Precision | Recall | F1 | Accuracy
Reference (97.37%) | 97.37 | 97.37 | 97.37 | 97.37
v2 + memory, message labels | 98.16 | 97.78 | 97.97 | 98.74
Abdel Hakeem & Kim, IEEE T-ITS 26(8), 2025 (survey), Table XIII: 97.37% for VeReMi, one number for accuracy, precision, recall and F1.
Not like-for-like: that figure is on the original VeReMi (5 attacks) and its source is not cited. Under vehicle labels our recall (96.09) and F1 (97.12) are below it.
Notes: Report the comparison with its caveat; do not claim we beat the reference outright. This chart is the 14-attack system; on 18 attacks (with Sybil) all four numbers are below 97.37, see next slide.

## Slide 9
Extension: 18 attacks, including Sybil
18 attacks, 88,695 test windows | Precision | Recall | F1 | Accuracy
Ours, message labels | 96.30 | 95.46 | 95.88 | 97.04
Ours, vehicle labels | 96.33 | 94.44 | 95.38 | 96.66
No neighbour attention, message | 96.28 | 92.69 | 94.45 | 96.07
Sybil attack | Recall
GridSybil (largest, 20,598 slots) | 0.823
DataReplaySybil | 0.914
DoSDisruptiveSybil | 0.969
DoSRandomSybil | 0.997
Senders are tracked by pseudonym (what a receiver sees); three new inputs: identity age, handover distance, lockstep. Final = mean of 3 models. Message-label FPR 2.07%.
Neighbour attention helps more with Sybil: +1.4 F1 (vs +0.3 on 14 attacks).
Honest result: on 18 attacks all four numbers are below the 97.37% reference. Missed GridSybil ghosts look honest on every content check; they need an independent signal.
All values in % except recall per attack (message labels). Source: results/results_v18_final.json, paper/tables_v18.tex.
Notes: The 14-attack results are unchanged. Sybil makes the task harder: fake identities are separate senders. On the 14 original attack runs this model's FPR is 1.6% (vs 0.6% for the 14-attack model) because it lowers its threshold to catch ghosts. A bigger model alone and receiver memory did not help.

## Slide 10
Open items and next steps
GridSybil ghosts that look honest on every content check (recall 0.823)
Check on original VeReMi and VeReMi NextGen
Run v2 on dense traffic; add a 3rd seed
On-road consistent lies need an independent signal: signal strength, on-board sensors, roadside units
Paper done: paper/main.pdf, IEEE conference format, 6 pages, 18 references